## Slide 1
Algorithm Design and Analysis
Session 10
Strassen’s Matrix Multiplication

## Slide 2: Basic Matrix Multiplication
Strassen’s Matrix Multiplication
void matrix_mult (){
for (i = 1; i <= N; i++) {
for (j = 1; j <= N; j++) {
for(k=1; k<=N; k++){
C[i,j]=C[i,j]+A[i,k]*B[k,j]; }
}}
Time complexity of above algorithm is
T(n)=O(n3)
Let A an B two n×n matrices. The product C=AB is also an n×n matrix.

## Slide 3: Divide and Conquer technique
We want to compute the product C=AB, where each of A,B, and C are n×n matrices.
Assume n is a power of 2.
If n is not a power of 2, add enough rows and columns of zeros.
We divide each of A,B, and C into four n/2×n/2 matrices, rewriting the equation C=AB as follows:

## Slide 4
Then,
C11=A11B11+A12B21
C12=A11B12+A12B22
C21=A21B11+A22B21
C22=A21B12+A22B22
Each of these four equations specifies two multiplications of n/2×n/2 matrices and the addition of their n/2×n/2 products.
We can derive the following recurrence relation for the time T(n) to multiply two n×n matrices:
T(n)= c1 if n<=2
8T(n/2)+ c2n2 if n>2
T(n) = O(n3)
This method is no faster than the ordinary method.
c11
c12
c22
c21
A11
A12
A21
A22
B21
B22
B11
B12

## Slide 5
Substitution Method:
T(n)= 8T(n/2)+ c2n2
=8 8T(n/4)+ c2(n/2)2 + c2n2
= 82 T(n/4)+ c22n2 + c2n2
=82 8T(n/8)+ c2(n/4)2 + c22n2 + c2n2
=83 T(n/8)+ c24n2 + c22n2 + c2n2
:
=8kT(1)+ ………………+ c24n2 + c22n2 + c2n2
= 8log2n c1 + c n2
=nlog2 c1 + c n2 = n3 c1+ cn2 = O(n3 )
.
8

## Slide 6
Strassen’s method
Matrix multiplications are more expensive than matrix additions or subtractions( O(n3) versus O(n2)).
Strassen has discovered a way to compute the multiplication using only 7 multiplications and 18 additions or subtractions.
His method involves computing 7 n×n matrices M1,M2,M3,M4,M5,M6, and M7, then cij’s are calculated using these matrices.

## Slide 7: Formulas for Strassen’s Algorithm
M1 = (A11 + A22)  (B11 + B22)
M2 = (A21 + A22)  B11
M3 = A11  (B12 – B22)
M4 = A22  (B21 – B11)
M5 = (A11 + A12)  B22
M6 = (A21 – A11)  (B11 + B12)
M7 = (A12 – A22)  (B21 + B22)
C11=M1 + M4 - M5 + M7
C12= M3 + M5
C21= M2 + M4
C22=M1 + M3 - M2 + M6

## Slide 8
    C11 C12 A11 A12 B11 B12
    = *
    C21 C22 A21 A22 B21 B22
    M1 + M4 - M5 + M7 M3 + M5
    =
    M2 + M4 M1 + M3 - M2 + M6
The resulting recurrence relation for T(n) is
T(n)= c1 n<=2
7T(n/2) +c2n2 n>2

## Slide 9
T(n)= 7kT(1) + c2n2 1+ 7/4 + (7/4)2 + (7/4) 3+……………..+ (7/4)k-1
= 7log2n c1 +c2 n2 (7/4)log2n
= nlog27 + nlog24 ( n log27-log24 )
=2 nlog27 = O(nlog27) ~ O( n2.81)

## Slide 10: Div. & Conq. : Strassen’s Matrix Multiplication
Recurrence for
# of multiplications is
M(n) = 7M(n/2) for n > 1
M(1) = ?
For n = 2m,
M(n) = 7M(n/2) = 72M(n/22)
M(n) = 7m M(n/2m)
= 7m = 7lgn
= nlg7 ≈ n2.807
For # of adds/subs,
Using Master thm,
A(n) є Θ(nlg7) better
than brute-force’s Θ(n3)
ALGORITHM Strassen(A, B, n)
//Input: A and B are n×n matrices
//where n is a power of two
//Output: C = A*B
if n = 1
return C = A*B
else
Partition A = and B =
where the blocks Aij and Bij are (n/2)-by-(n/2)
M1 <- Strassen(A00+A11, B00+B11, n/2)
M2 <- Strassen(A10+A11, B00, n/2)
M3 <- Strassen(A00, B01-B11, n/2)
M4 <- Strassen(A11, B10-B00, n/2)
M5 <- Strassen(A00+A01, B11, n/2)
M6 <- Strassen(A10-A00, B00+B01, n/2)
M7 <- Strassen(A01-A11, B10+B11, n/2)
C00 <- M1+M4-M5+M7
C01 <- M3+M5
C10 <- M2+M4
C11 <- M1+M3-M2+M6
return C =
A00 A01
A10 A11
B00 B01
B10 B11
C00 C01
C10 C11
A(n) = 7A(n/2)+18(n/2)2 for n > 1
A(1) = 0
DONE WITH STRASSEN!

## Slide 11: Div. & Conq. : Strassen’s Matrix Multiplication
How do we multiply two 2×2 matrices in general method ?
2
3 4
3 5
1 4
=
1*3+2*1=5 1*5+2*4=13
3*3+4*1=13 3*5+4*4=31
How many multiplications
and additions did we need?

## Slide 12: STRESSEN’S MATRIX MULTIPLICATION
P1 = (A11+ A22)(B11+B22)
P2 = (A21 + A22) * B11
P3 = A11 * (B12 - B22)
P4 = A22 * (B21 - B11)
P5 = (A11 + A12) * B22
P6 = (A21 - A11) * (B11 + B12)
P7 = (A12 - A22) * (B21 + B22)
C11 = P1 + P4 - P5 + P7
C12 = P3 + P5
C21 = P2 + P4
C22 = P1 + P3 - P2 + P6
A11 | A12
A21 | A22
x
=
B11 | B12
B21 | B22
C11 | C12
C21 | C22

## Slide 13: Div. & Conq. : Strassen’s Matrix Multiplication
By using Strassen method
a00 a01
a10 a11
=
b00 b01
b10 b11
c00 c01
c10 c11
=
m1+m4-m5+m7 m3+m5
m2+m4 m1+m3-m2+m6
m1 = (a00+a11)*(b00+b11) = 35
m4 = a11*(b10-b00) = -8
m6 = (a10-a00)*(b00+b01) = 16
m2 = (a10+a11)*b00 =21
m5 = (a00+a01)*b11 = 12
m7 = (a01-a11)*(b10+b11) = -10
m3 = a00*(b01-b11) = 1
7 multiplications
18 additions/subtractions
35-8-12-10=5 1+12=13
21-8=13 35+1-21+16=31

## Slide 14: STRESSEN’S MATRIX MULTIPLICATION
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
1 | 0 | 0 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
0 | 0 | 0 | 1
x
=
P1 = (A11+ A22)(B11+B22)
P2 = (A21 + A22) * B11
P3 = A11 * (B12 - B22)
P4 = A22 * (B21 - B11)
P5 = (A11 + A12) * B22
P6 = (A21 - A11) * (B11 + B12)
P7 = (A12 - A22) * (B21 + B22)
C11 = P1 + P4 - P5 + P7
C12 = P3 + P5
C21 = P2 + P4
C22 = P1 + P3 - P2 + P6
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16

## Slide 15: STRESSEN’S MATRIX MULTIPLICATION
P1 = (A11+ A22)(B11+B22)
P2 = (A21 + A22) * B11
P3 = A11 * (B12 - B22)
P4 = A22 * (B21 - B11)
P5 = (A11 + A12) * B22
P6 = (A21 - A11) * (B11 + B12)
P7 = (A12 - A22) * (B21 + B22)
C11 = P1 + P4 - P5 + P7
C12 = P3 + P5
C21 = P2 + P4
C22 = P1 + P3 - P2 + P6
1 | 2
5 | 6
A11=
3 | 4
7 | 8
A12=
9 | 10
13 | 14
A21=
11 | 12
15 | 16
A22=
1 | 0
0 | 1
B11=
0 | 0
0 | 0
B12=
0 | 0
0 | 0
B21=
1 | 0
0 | 1
B22=

## Slide 16: STRESSEN’S MATRIX MULTIPLICATION
C11 = A11+B11
C12 = A12+B12
C21 = A21+B21
C22 = A22+B22
A11 | A12
A21 | A22
+
=
B11 | B12
B21 | B22
C11 | C12
C21 | C22

## Slide 17
Ex: Multiply the following two matrices using Strassen’s Matrix Multiplication
1 2 3 4
5 6 7 8
9 10 11 12
13 14 15 16
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1

## Slide 18: Ex:2

## Slide 19
Thank You